## Slide 1: CHECKSUM
 A checksum is a count of the number of bits in a transmission unit that is included with the unit so that the receiver can check to see whether the same number of bits arrived.
 If the counts match, it's assumed that the complete transmission was received and there is no error in the packet.
 Otherwise if the count doesn’t matches then it’s assumed as the transmission was incomplete and contains error.

## Slide 2: Methodology
 Let’s have a data of ( 7,11,12,0,6 ) this data can be represented into four bits.
 At first we need to take the sum of all the data ( 7+11+12+0+6 = 36 ).
 Sender sends the data along with ( -36 )
 This all data can be represented into 4 bits.
 But not the sum ( -36 ) it is more than 4 bits.
 SUM = 36 + ( -36 ) = 0
 Which means there’s no error.
7 11 12 0 6 -36

## Slide 3: Example
 For eg: 21
8 2
1 0 1 0 1
1
0 1 1 0
By taking 1’s Comp
1 0 0 1
Converting Hexadecimal To Binary Here we need 4 digits
So bring last digit & add Wrapped Sum = 6 Check Sum = 9
16
1
4

## Slide 4: Sender Side
Data 7,11,12,0,6
Sum = 36 32 16 8 4 2 1
1 0 0 1 0 0
bringing last 1 0 down & add 1 0
1’s Complement
0 | 1 | 1 | 0 | Wrapped Sum = 6
1 | 0 | 0 | 1 | Check Sum = 9

## Slide 5: Receiver Side
Here we add all data along with checksum Sum + checksum = 36 + 9 = 45
32 16 8 4 2 1
1 0 1 1 0 1
bringing last 1 0 down & add 1 0
 | 1 | 1 | 1 | 1 | Wrapped Sum = 15
1’s Complement So There’s no any error. | 0 | 0 | 0 | 0 | Check Sum = 0